## Slide 1: NAT Traversal for VoIP
Jonathan Rosenberg
Cisco Fellow

## Slide 2: What is NAT?
Network Address Translation (NAT)
  Creates address binding between internal private and external public address
  Modifies IP Addresses/Ports in Packets
  Benefits
    Avoids network renumbering on change of provider
    Allows multiplexing of multiple private addresses into a single public address ($$ savings)
    Maintains privacy of internal addresses
Client
N
A
T
N
A
T
S: 1.2.3.4:8877
D: 67.22.3.1:80
Binding Table
Internal External
10.0.1.1:6554 -> 1.2.3.4:8877
S: 10.0.1.1:6554
D: 67.22.3.1:80
IP Pkt
IP Pkt

## Slide 3: Why is this bad for SIP?
Client will generate SIP INVITE and 200 OK responses with private addresses
  In the SDP as the target for receipt of media
  In the Contact of a REGISTER as the target for incoming INVITE
  In the Via of a request as the target for the response
Recipient will not be able to send packets to this private address
  Media is discarded
  Incoming calls are not delivered
  Responses are not received
Client
N
A
T
INVITE
Send media to 10.0.1.1:8228

## Slide 4: Why is this bad for SIP?
Client will generate SIP INVITE and 200 OK responses with private addresses
  In the SDP as the target for receipt of media
  In the Contact of a REGISTER as the target for incoming INVITE
  In the Via of a request as the target for the response
Recipient will not be able to send packets to this private address
  Media is discarded
  Incoming calls are not delivered
  Responses are not received
Client
N
A
T
INVITE
Send media to 10.0.1.1:8228
Hardest problem, solved by ICE
Solved by SIP Outbound
Solved by rport (RFC 3581)

## Slide 5: Solution Space
Application Layer Gateways (ALGs)
Session Border Controllers (SBC)
Simple Traversal of UDP Through NAT (STUN)
Traversal Using Relay NAT (TURN)
Universal Plug N Play (UPnP)
Interactive Connectivity Establishment (ICE)

## Slide 6: ALG: The obvious solution?
The NAT rewrites source IP of SIP packet, but not contents
Why not have NAT rewrite the contents of the SIP packet also (Application Layer Gateway (ALG))?
Numerous big problems
  Requires SIP security mechanisms to be disabled
  Hard to diagnose problems
  Requires network upgrade in all NAT
  Frequent implementation problems
  Incentives mismatched
  Anathema to the concept of the Internet
Client
N
A
T
INVITE
Send media to 1.2.3.4:6290
INVITE
Send media to 10.0.1.1:8228
S: 10.0.1.1:6554
D: 67.22.3.1:80
S: 1.2.3.4:8877
D: 67.22.3.1:80
Binding Table
Internal External
10.0.1.1:6554 -> 1.2.3.4:8877
10.0.1.1:8228 -> 1.2.3.4:6290

## Slide 7: Session Border Controllers (SBC)
Close cousin of the ALG
Client pointed to SBC as its outbound proxy
SBC forwards requests to actual SIP proxy
When receiving an INVITE from client, SBC rewrites SDP to point to itself
SIP
Proxy
INVITE
SBC
INVITE
Send media to 10.0.1.1:8228
INVITE
Send media to 1.2.3.4:800
NAT

## Slide 8: Session Border Controllers (SBC)
When 200 OK is received by SBC, it rewrites SDP to point to itself again
  Different port than used in offer
SIP
Proxy
200 OK
SBC
200 OK
Send media to 1.2.3.4:802
200 OK
Send media to 12.13.14.15:100
NAT

## Slide 9: Session Border Controllers (SBC)
End result is that each agent will send RTP packets towards the SBC
This creates a binding in intervening NAT
SBC remembers source IP of RTP packets from each side
SBC relays packets back towards each source
SIP
Proxy
SBC
NAT
RTP
Packets

## Slide 10: Classic STUN
Client discovers presence and type of NAT at startup
If NAT is a ‘good’ NAT, it can use STUN
At call setup time, gathers a server reflexive candidate from STUN server and includes it in m/c-line of INVITE
Problems
  Doesn’t work with ‘bad’ NAT
  Doesn’t work if both behind same NAT
  NAT type classification known to be inaccurate
STUN Request
STUN
Response
1.2.3.4:8866
INVITE
1.2.3.4:8866
200 OK
ACK
RTP
NAT
STUN
Server
SIP
Proxy

## Slide 11: TURN
At call setup time, agent gathers a relayed candidate from STUN relay server and includes it in m/c-line of INVITE
Call flow much like STUN case
Media always relayed through STUN relay
STUN Request
STUN
Response
9.7.6.5:8866
INVITE
9.7.6.5:8866
200 OK
ACK
RTP
NAT
STUN
Server
SIP
Proxy

## Slide 12: UPnP
Universal Plug N Play
Similar to STUN, in that client learns its IP and port on the public side of NAT
However, client talks to the NAT, not through it
  No separate STUN server
NAT discovered via multicast
UPnP Request
UPnP
Response
9.7.6.5:8866
INVITE
9.7.6.5:8866
200 OK
ACK
RTP
NAT
SIP
Proxy

## Slide 13: ICE Step 1: Allocation
Before Making a Call, the Client Gathers Candidates
Each candidate is a potential address for receiving media
Three different types of candidates
  Host Candidates
  Server Reflexive Candidates
  Relayed Candidates
Relay
Host
Candidates reside on the agent itself
Server Reflexive candidates
are addresses residing on a NAT
NAT
NAT
Relayed candidates reside on a host acting as a relay towards the agent

## Slide 14: Using STUN to Obtain Candidates
Server reflexive and relayed candidates are learned by talking to a STUN server using the Relay Usage
Client sends query to STUN relay server
Query passes through NAT, creates bindings
STUN relay server allocates a relayed address and also reports back source address of request to client
  This will be the server reflexive address
STUN
Server
1.2.3.4:1000
NAT
NAT
12.13.14.15:8200
10.0.1.1:500
Allocate
Request
Allocate
Response reflexive=1.2.3.4:1000 relayed=12.13.14.15:8200

## Slide 15: ICE Step 2: Prioritization
Type-Preference: Preference for type (host, server reflexive, relayed)
  Usually 0 for relayed, 126 for host
Local Preference: Amongst candidates of same type, preference for them
  If host is multihomed, preference by interface
  If host has multiple STUN servers, preference for that server
Component ID as described previously
This algorithm is only SHOULD strength
priority = (2^24)*(type preference)
+(2^8)*(local preference)
+(2^0)*(256 - component ID)
Local Preference
Component ID
Type Preference
32 bits

## Slide 16: Encoding the Offer
Each candidate is placed into an a=candidate attribute of the offer
Each candidate line has
  IP address and port
  Component ID
  Foundation
  Transport Protocol
  Priority
  Type
  “Related Address”
v=0
o=jdoe 2890844526 2890842807 IN IP4 10.0.1.1
s=
c=IN IP4 192.0.2.3
t=0 0
a=ice-pwd:asd88fgpdd777uzjYhagZg
a=ice-ufrag:8hhY
m=audio 45664 RTP/AVP 0
a=rtpmap:0 PCMU/8000
a=candidate:1 1 UDP 2130706178 10.0.1.1 8998 typ local
a=candidate:2 1 UDP 1694498562 192.0.2.3 45664 typ srflx raddr 10.0.1.1 rport 8998

## Slide 17: ICE Step 3: Initiation
Caller sends a SIP INVITE as normal
No ICE processing by proxies
SIP itself traverses NAT using SIP outbound and rport
SIP
Proxy
INVITE

## Slide 18: ICE Step 4: Allocation
Called party does exactly same processing as caller and obtains its candidates
Recommended to not yet ring the phone!
STUN
Server
NAT
NAT
Allocate
Request
Allocate
Response

## Slide 19: ICE Step 5: Information
Caller sends a provisional response containing its SDP with candidates and priorities
  Can also happen in 2xx, but this flow is “best”
Provisional response is periodically retransmitted
As with INVITE, no processing by proxies
Phone has still not rung yet
SIP
Proxy
1xx

## Slide 20: ICE Step 6: Verification
Each agent pairs up its candidates (local) with its peers (remote) to form candidate pairs
Each agent sends a connectivity check every 20ms, in pair priority order
  Binding Request from the local candidate to the remote candidate
Upon receipt of the request the peer agent generates a response
  Contains a mapped address indicating the source IP and port seen in the request
If the response is received the check has succeeded
STUN
Server
NAT
NAT
STUN
Server
NAT
NAT
1
2
3
4
5

## Slide 21: Peer Reflexive Candidates
Connectivity checks can produce additional candidates
  Peer reflexive candidates
Typically happens when there is a symmetric NAT between users
Peer reflexive candidate will be discovered by both users
  For user A, from the Response
  For user B, from the Request
Allows direct media even in the presence of symmetric NAT!
Sym
NAT
NAT allocates new binding towards B
STUN Request
STUN Response
A
B
B informs A of new binding
A learns a new local candidate towards B!

## Slide 22: ICE Step 7: Coordination
ICE needs to finalize on a candidate pair for each component of each media stream
  More than one may work
Each agent needs to conclude on the same set of pairs
Finalization takes place without SIP signaling – all through STUN
  One agent acts as the ‘controlling’ agent
  Controlling agent includes a flag in its STUN request indicating completion

## Slide 23: ICE Step 8: Communication
Media can flow in each direction once pairs have been selected by the controlling agent for each component
Allows “early media” in both directions
STUN
Server
NAT
NAT
STUN
Server
NAT
NAT

## Slide 24: ICE Step 9: Confirmation
200 OK and ACK work as normal
  200 mirrors SDP from provisional
If m/c-line in original INVITE didn’t match candidate pairs selected by ICE, controlling agent does a re-INVITE to place them in m/c-line
Re-INVITE ensures that ‘middleboxes’ have the correct media address
  QoS installation (i.e., IMS or Packetcable)
  Diagnostic tools
  Monitoring applications
  Firewalls
Offerer
Answerer
Re-INVITE
200 OK
200 OK
ACK
ACK

## Slide 25: Comparison: Metrics
Requires client changes?
Requires proxy changes?
Requires addition of new box?
Requires NAT support?
Reduces or eliminates usage of relays?
Good security?
Works through broad range of NAT and firewalls?
Works for other applications besides SIP?
Fast call setup?
Operator cost?

## Slide 26: Comparison Table
Criteria | ALG | SBC | STUN | TURN | UPnP | ICE
Client Changes? | N | N | Y | Y | Y | Y
Proxy Changes? | N | Y (SBC) | N | N | N | N
NAT Changes? | Y | N | N | N | Y | N
New Box? | N | Y | Y | Y | N | Y
Minimize Relays? | Mostly | No | Yes when it works | No | Mostly | Yes
Security | Awful | Not great | Good | Good | Awful | Excellent
Works broadly? | No (has to be there) | Mostly – no TCP story | No | Yes | No (has to be there) | Yes
Non-SIP? | Yes | No | Yes | Yes | Yes | Yes
Fast call setup? | No increase | No increase | Slight increase | Slight increase | Slight increase | Moderate increase
Operator Cost | N/A | Very high | Moderate | High | N/A | Minimal possible
Areas of ICE strengths

## Slide 27: Market Adoption of NAT Technologies
Enterprises
  SIP support needed primarily for Centrex
  Mostly provided by ALG
    Some SBC support
  Beginning interests in ICE through MSFT
Facilities-Based Service Providers
  Almost entirely SBCs
  Cable now formally adopting ICE in Packetcable 2.0
  Being added as optional in IMS R7 though some challenges remain in wireless applicability
Application Service Providers
  Mix of SBCs, STUN and ICE
  ICE is attractive here due to cost minimization