## Slide 2: A Tutorial on SIP
Jonathan Rosenberg
Chief Scientist

## Slide 3: Introducing - Session Initiation Protocol (SIP)
Developed in mmusic group in IETF
  Proposed standard RFC2543, Feb. 1999
  Work began 1995
  Part of Internet Multimedia Conferencing Suite
Main functions
  Invitation of users to sessions
    Find the users current location to deliver invitation
    Carry opaque session descriptions
  Modification of sessions
  Termination of sessions
Main Features
  Personal mobility services
  Wide area operation
  Session independence
    voice, video, games, chat, virtual reality, etc.
  Leverages other Internet protocols

## Slide 4: Basic Design
SIP is a Client Server Protocol
  Clients send requests, receive responses
  Servers receive requests, send responses
Modelled after HTTP
Each request invokes method on server
  Main purpose of request
Messages contain bodies
Client
Server
request
response

## Slide 5: Transactions
Fundamental unit of messaging exchange
  Request
  Zero or more provisional responses
  Usually one final response
  Maybe ACK
All signaling composed of independent transactions
Identified by Cseq
  Sequence number
  Method tag
C
S
INVITE
100
200
ACK
BYE
200
First Transaction
Second Transaction
Cseq: 1
Cseq: 2

## Slide 6: Session Independence
Body of SIP message used to establish call describes the session
Session could be
  Audio
  Video
  Game
SIP operation is independent of type of session
SIP Bodies are MIME objects
  MIME = Multipurpose Internet Mail Extensions
  Mechanisms for describing and carrying opaque content
  Used with HTTP and email
SIP bodies can carry other information too!
  JPEG for caller ID
  HTML page for Web IVR

## Slide 7: Protocol Components
User Agent Client (UAC)
  End systems
  Send SIP requests
User Agent Server (UAS)
  Listens for call requests
  Prompts user or executes program to determine response
User Agent
  UAC + UAS
Redirect Server
  “Network” server; redirects users to try other server
Proxy Server
  “Network Server” Proxies request to another server Can “fork” request to multiple servers, creating a search tree
Registrar
  receives registrations regarding current user locations

## Slide 8: SIP Addressing
SIP addresses are URL’s
URL contains several components
  Scheme (sip)
  Username
  Optional password
  Hostname
  Optional port
  Parameters
  Headers and Body
SIP allows any URI type
  tel URIs
  http URLs for redirects
  mailto URLs
  leverage vast URI infrastructure
sip:jdrosen@dynamicsoft.com:5061;
user=host?Subject=foo

## Slide 9: Network Servers
Main Function is routing
  Where should request go next?
  Can redirect or proxy there
SIP does not dictate how routing is done
Location Service provides data
  Abstract concept
  LDAP, whois, whois++
  result of program execution (IN)
End result is a mapping from one SIP URI to another
  sip:jdrosen@dynamicsoft.com to sip:jdrosen@eagle.dynamicsoft.com
Proxy
LS

## Slide 10: Proxies
Requests can traverse multiple proxies from caller to callee
Each proxy:
  receives request
  checks if domain in request URI is its own
Domain matches
  invokes location service
  obtains new request URI
  looks up host portion in DNS
  forwards to next hop server
  receives response
  forwards response
Proxy
LS
sip:joe@a.com
sip:j_user@eng.a.com
Proxy
sip:j_user@host. eng.a.com
200 OK
200 OK
200 OK

## Slide 11: DNS Usage
Take domain name of request URI
Look for SRV records
  SRV records specify a list of IP addresses for servers for a particular service
  List includes priority values and preferences for each address
Try IP addresses in order of preference, go to next if no response
If no SRV records present, use A records
  A records are standard hostname to IP address records
DNS
Proxy
DNS SRV
Query
A 100
B 200
C 300
D 400
A
B
C
D

## Slide 12: Local Outbound Proxies
Can send a request to a proxy without performing DNS procedure
Result is that proxy receives a request whose domain is not its own
Proxy then performs DNS process just described to forward request
May also provide additional services
  Outbound screening
  Authorization
  Logging
  Firewall control
a.com
INVITE joe@b.edu
INVITE joe@b.edu

## Slide 13: SIP Methods
INVITE
  Invites a participant to a session
  idempotent - reINVITEs for session modification
BYE
  Ends a client’s participation in a session
CANCEL
  Terminates a search
OPTIONS
  Queries a participant about their media capabilities, and finds them, but doesn’t invite
ACK
  For reliability and call acceptance
REGISTER
  Informs a SIP server about the location of a user

## Slide 14: SIP Architecture
Request
Response
Media
1
2
3
4
5
6
7
8
9
10
11
12
SIP UA
SIP Redirect
Server
SIP Proxy
SIP Proxy
SIP UA
(User Agent Server)
Location Service
13
14

## Slide 15: SIP Message Syntax
Many header fields from http
Payload contains a media description
  SDP - Session Description Protocol
INVITE sip:ann@lucent.com SIP/2.0
From: J. Rosenberg <sip:jdrosen@dynamicsoft.com>
Subject: SIP will be discussed, too
To: A. Netravali <sip:ann@lucent.com>
Via: SIP/2.0/UDP pc13.dynamicsoft.com
Call-ID: 1997234505.56.78@122.3.44.12
Content-type: application/sdp
CSeq: 4711 INVITE
Content-Length: 187
v=0
o=user1 53655765 2353687637 IN IP4 128.3.4.5
s=Mbone Audio
i=Discussion of Mbone Engineering Issues
e=mbone@somewhere.com
c=IN IP4 224.2.0.1/127
t=0 0
m=audio 3456 RTP/AVP 0

## Slide 16: SIP Address Fields
Request-URI
  Contains address of next hop server
  Rewritten by proxies based on result of Location Service
To
  Address of original called party
  Contains optional display name
From
  Address of calling party
  Optional display name
INVITE sip:ann@lucent.com SIP/2.0
From: J. Rosenberg
<sip:jdrosen@dynamicsoft.com>;tag=76ah
Subject: SIP will be discussed, too
To: A. Netravali <sip:ann@lucent.com>
Via: SIP/2.0/UDP pc13.dynamicsoft.com
Call-ID: 1997234505.56.78@122.3.44.12
Content-type: application/sdp
Contact: sip:jdrosen@pc13.dynamicsoft.com
CSeq: 4711 INVITE
Content-Length: 187
v=0
o=user1 53655765 2353687637 IN IP4 128.3.4.5
s=Mbone Audio
i=Discussion of Mbone Engineering Issues
e=mbone@somewhere.com
c=IN IP4 224.2.0.1/127
t=0 0
m=audio 3456 RTP/AVP 0

## Slide 17: SIP Responses
Look much like requests
  Headers, bodies
Differ in top line
  Status Code
    Numeric, 100 - 699
    Meant for computer processing
    Protocol behavior based on 100s digit
    Other digits give extra info
  Reason Phrase
    Text phrase for humans
    Can be anything
Status Code Classes
  100 - 199 (1XX): Informational
  200 - 299 (2XX): Success
  300 - 399 (3XX): Redirection
  400 - 499 (4XX): Client Error
  500 - 599 (5XX): Server Error
  600 - 699 (6XX): Global Failure
Two groups
  100 - 199: Provisional
    Not reliable
  200 - 699: Final, Definitive
Example
  200 OK
  180 Ringing

## Slide 18: Example SIP Response
Note how only difference is top line
Rules for generating responses
  Call-ID, To, From, Cseq are mirrored in response to support matching
  Tag added to To field
SIP/2.0 200 OK
From: J. Rosenberg
<sip:jdrosen@dynamicsoft.com>;tag=76ah
To: A. Netravali <sip:ann@lucent.com>;tag=112
Via: SIP/2.0/UDP pc13.dynamicsoft.com
Call-ID: 1997234505.56.78@122.3.44.12
CSeq: 4711 INVITE
Contact: sip:ann@lucent3.lucent.com

## Slide 19: SIP Transport
SIP Messages over UDP or TCP
Reliability mechanisms defined for UDP
UDP Preferred
  Faster
  No connection state needed in kernel
  Multicast possible (later)
Reliability mechanisms depend on SIP request method
  INVITE
  anything except INVITE
Reason: optimized for phone calls

## Slide 20: INVITE reliability
Client retransmits INVITE with exponential backoff
  500ms, 1s, 2s, 4s, 8s…..
Retransmissions cease when provisional response arrives
  Next hop should send 100 Trying to stop retransmissions
  Response retransmitted when request retransmissions arrive
Final response retransmitted with exponential backoff up to 4s
  May take a long time to answer phone!!
ACK sent on receipt of final response
C
S
INV
INV
INV
INV
Ring...
100 Trying
INV
100 Trying
200 OK
200 OK
ACK

## Slide 21: Non-INVITE Reliability
Responses should come quickly
  No need to ring phone
Request retransmitted w/ exponential backoff, up to 4s
  If provisional response received, request retransmitted at 4s intervals
After 4s, request retransmitted every 4s
Response retransmitted on receipt of request
  That’s why request must be retransmitted after provisional - protect against response loss
  no ACK
C
S
BYE
BYE
BYE
BYE
BYE
200 OK
100 Trying
BYE
200 OK

## Slide 22: TCP Transport
Reliability rules for TCP same as UDP with one change
  Requests not retransmitted
However, 2xx final responses still retransmitted
ACK is still sent
Reason?
  Handles case of a mix of UDP and TCP connections

## Slide 23: Hop by Hop vs. End to End
Reliability can be HBH or E2E
  HBH implies message transmitted reliably between each entity (UAC to proxy, proxy to UAS)
  E2E implies proxies simply forward requests, reliability assured between UAC and UAS only
SIP uses HBH reliability… almost
  Stateless proxies simply forward requests
  200 OK response to INVITE is E2E reliable!!!
    UAC must see all 200 OK
UAC
Proxy
UAS
INVITE
100 Trying
INVITE
100 Trying
INVITE
100 Trying
200 OK
200 OK
200 OK
200 OK
200 OK
ACK
200 OK
200 OK
ACK
ACK

## Slide 24: Registrations
Proxy needs to know where users are sitting
SIP REGISTER message allows clients to tell proxy servers
REGISTER properties
  Contains list of current locations in Contact headers
  Registrar identified in Request URI
  Identifies registered user in To field
  Identifies person performing registration in From field (usually = To)
  Expires header indicates desired lifetime
    Can be different for each Contact
  May be body
REGISTER sip:dynamicsoft.com SIP/2.0
To: Rosenberg <sip:jdrosen@dynamicsoft.com>
From: Claribel <sip:cpena@dynamicsoft.com>
Call-ID: 1997234505.56.78@122.3.44.12
CSeq: 123 REGISTER
Contact: sip:jdrosen@pc33.dynamicsoft.com
Contact: http://www.cs.columbia.edu/~jdrosen
Expires: 3600

## Slide 25: Registration Responses
Registrar behavior on receiving REGISTER
  check if domain is its own
  authorize user in From field
  Add address bindings of (To field) -> (Contact list)
  Lower expiration time if too long
  Return, in response, list of all current registrations
  Return, in response, expiration time for all registrations
SIP/2.0 200 OK
To: Rosenberg <sip:jdrosen@dynamicsoft.com>
From: Claribel <sip:cpena@dynamicsoft.com>
Call-ID: 1997234505.56.78@122.3.44.12
CSeq: 123 REGISTER
Contact: sip:jdrosen@pc33.dynamicsoft.com
Contact: http://www.cs.columbia.edu/~jdrosen
Contact: mailto:jdrosen@dynamicsoft.com
;expires=“Thu, 01 Dec 2002 16:00:00 GMT”
Expires: 3600

## Slide 26: Registration Details
User Agent must refresh registrations by resending before expiration
Each contact must be refreshed independently
  Can place them all in same REGISTER
  Can use separate REGISTER for each
Deleting Registrations
  Send a refresh with Expires: 0
Querying list of current registrations
  Send REGISTER with no Contact headers
  Response contains list of current registrations
Distributed registrations
  Registrations for the same user (I.e., same To field) can come from different hosts, each registering different contacts
  Example: my cell phone registers itself, my PC registers itself

## Slide 27: Forking
A proxy may have more than one address for a user
  Happens when more than one SIP URL is registered for a user
  Can happen based on static routing configuration
In this case, proxy may fork
Forking is when proxy sends request to more than one proxy at once
First 200 OK that is received is forwarded upstream
All other unanswered requests cancelled
INVITE
user@domain
INVITE user2@domain2
INVITE user3@domain3

## Slide 28: More on Forking
Main benefits
  Allows rapid “search” for user at many locations
  Phone rings more than one place at a time
Two variations
  Sequential Search: Try first address, only if that fails try second address
  Parallel Search: Try all addresses at once (as in previous slide)
Hybrid approaches possible
Many proxies can fork, resulting in tree of proxies
“Best” response to forked request is chosen and forwarded upstream
  First 200 OK received
  First 600 received if no 200 OK
  Lowest numbered response after all responses are received, given none was 200 or 600
  Note usually only one response is forwarded upstream

## Slide 29: CANCEL
CANCEL used to “take back” a request
Main application: stop phones from ringing which have not yet answered
Semantics
  Always refers to another request
  If you get a CANCEL, and haven’t answered request, answer request with 487. Answer CANCEL with 200.
  Can be generated by proxies or UA - usually proxies
UAC
Proxy
UAS
UAS
INV
INV
100
100
INV
100
200
200
CANCEL
OK
487
ACK
ACK

## Slide 30: Response Routing: Via
Responses take same path as requests
How does server know where to send response?
  Remember where request came from
  Place information in request, get it back in response!!
Via Header
  Traces path of request
  “Stack” header
    Each proxy pushes its address in requests
    Pops its address in responses
Via header reflected in response from UAS
When proxy receives response
  check if topmost Via is itself
  If yes, remove and check next header
  Send response to address in next Via
  If no next Via, response is for me

## Slide 31: Via Operation
Proxy
Proxy
UAC
UAS
Address: A
Address: B
Address: C
Address: D
Via: A
Via: B Via: A
Via: C Via: B Via: A
Via: C Via: B Via: A
Via: B Via: A
Via: A
Request
Response

## Slide 32: Received Tags
Many cases where address in via is wrong!
  NAT
  Multihomed hosts
Rather, source address of packet is more correct
Solution: receive tag
  If source address of packet doesn’t equal top via address
  Proxy inserts received parameter into via header
  Indicates source IP address
  That address is used to send responses
End result
  Responses sent to source IP address of request, but to port in via header
  Strange combination, but it works well for multihomed hosts
INVITE sip:ann@lucent.com SIP/2.0
From: sip:jdrosen@dynamicsoft.com;tag=76ah
To: sip:ann@lucent.com
Via: SIP/2.0/UDP
pc13.dynamicsoft.com;received=12.3.2.1

## Slide 33: Stateful vs. Stateless Proxies
Stateless Proxy Definition
  Receives request, acccess location services, forwards request
  Forgets it even saw request after forwarding it
  When response comes, uses Via header to figure out where to send it
Stateful Proxy Definition
  Remembers it saw the request after forwarding it
  Can apply additional logic after response arrives
A proxy must be stateful when
  It forks (this requires special processing of responses to “remember” best one)
  It sends a request using multicast
  It uses TCP
Stateful vs. Stateless
  Stateless scales very well
    No memory requirements
    Tiny socket requirements
  Stateful is better for services
  Each proxy can independently decide which to be
Call Stateful
  Remembers multiple transactions being associated with a call

## Slide 34: Loop Detection
With all this forking and forwarding, request may hit the same proxy twice!
Need mechanisms to prevent this from looping forever
SIP provides two
  Max-Forwards
    Counter decremented by 1 on each hop
    Discard request when zero
  Via based loop prevention and detection
    Every proxy inserts address
    Check for my address when request comes

## Slide 35: Loop Detection: Details
Spirals
  When request hits server twice, but with different request URI
  Example: joe@example.com forwards to bob@example.com!
  Not an error
Must detect difference between loop and spiral
Solution
  Via header contains branch ID parameter
  Branch ID has two components
Branch ID Component 1
  When a proxy forks, each fork has a different component 1, so response associated with forked request
Branch ID Component 2
  Hash of To, From, Call-ID, Cseq and incoming request URI
  When you receive a request, check for Via headers with your own address
  For those with that address, recompute hash, see if it matches value in branch ID
  If match, loop, if not, spiral

## Slide 36: Routing of Subsequent Requests
Initial SIP request sent through many proxies
No need per se for subsequent requests to go through proxies
Each proxy can decide whether it wants to receive subsequent requests
  Inserts Record-Route header containing its address
For subsequent requests, users insert Route header
  Contains sequence of proxies (and final user) that should receive request
Proxy
Proxy
Proxy
UA1
UA2
INVITE
BYE

## Slide 37: Construction of Route Header
Each proxy may insert a RR
  Stack property
  Any URL meeting two requirements
    Routes back to that server
    Identifies the target recipient in some way
UAS reflects all RR in 200 OK Response
  Proxies can modify RR they inserted
  Allows Route for UAC/UAS to be different, which it should be!
UAC Constructs Route
  Flips order of Route headers
  Places Contact from 200 OK at bottom
  Result is Route set
UAS Constructs Route
  Takes RR from INVITE
  Adds Contact from INVITE at the end

## Slide 38: Example Route Construction
Proxy
Proxy
UAC
UAS
Addr: B Domain: t
Addr: C Domain: t2
Sip:b@t3
INV sip:b@t2 m:sip:a@o RR:sip:a@o;maddr=B
Sip:a@o
INV sip:b@t m: sip:a@o
INV sip:b@t3 m:sip:a@o RR:sip:a@o;maddr=C RR:sip:a@o;maddr=B
SIP/2.0 200 OK m:sip:b@t3 RR:sip:a@o;maddr=C RR:sip:a@o;maddr=B
SIP/2.0 200 OK m:sip:b@t3 RR:sip:b@t2;maddr=C RR:sip:a@o;maddr=B
SIP/2.0 200 OK m:sip:b@t3 RR:sip:b@t2;maddr=C RR:sip:b@t;maddr=B
UAC Route:
Sip:b@t;maddr=B,
Sip:b@t2;maddr=C
Sip:b@t3
UAS Route:
Sip:a@o;maddr=C,
Sip:a@o;maddr=B
Sip:a@o

## Slide 39: Setting up the Session
INVITE contains the Session Description Protocol (SDP) in the body
SDP conveys the desired session from the callers perspective
  Session consists of a number of media streams
  Each stream can be audio, video, text, application, etc.
Also contains information needed about the session
  codecs
  addresses and ports
SDP also conveys other information about session
  Time it will take place
  Who originated the session
  subject of the session
  URL for more information
SDP origins are multicast sessions on the mbone
  Originator of INVITE is not originator of session

## Slide 40: Anatomy of SDP
SDP contains informational headers
  version (v)
  origin(o) - unique ID
  information (I)
Time of the session
Followed by a sequence of media streams
Each media stream contains an m line defining
  port
  transport
  codecs
Media Stream also contains c line
  Address information
v=0
o=user1 53655765 2353687637 IN IP4 128.3.4.5
s=Mbone Audio
i=Discussion of Mbone Engineering Issues
e=mbone@somewhere.com
t=0 0
m=audio 3456 RTP/AVP 0 78
c=IN IP4 1.2.3.4
a=rtpmap:78 G723
m=video 4444 RTP/AVP 86
c=IN IP4 1.2.3.4
a=rtpmap:86 H263

## Slide 41: Negotiating the Session
Called party receives SDP offered by caller
Each stream can be
  accepted
  rejected
Accepting involves generating an SDP listing same stream
  port number and address of called party
  subset of codecs from SDP in request
Rejecting indicated by setting port to zero
Resulting SDP returned in 200 OK
Media can now be exchanged
v=0
o=user2 16255765 8267374637 IN IP4 4.3.2.1
t=0 0
m=audio 3456 RTP/AVP 0
c=IN IP4 4.3.2.1
m=video 0 RTP/AVP 86
c=IN IP4 4.3.2.1
Audio stream accepted, PCMU only.
Video stream rejected

## Slide 42: Changing Session Parameters
Once call is started, session can be modified
Possible changes
  Add a stream
  Remove a stream
  Change codecs
  Change address information
Call hold is basically a session change
Accomplished through a re-INVITE
Same session negotiation as INVITE, except in middle of call
Rejected re-INVITE - call still active!
C
S
INVITE
200
ACK
INVITE
200
ACK
reINVITE

## Slide 43: Hanging Up
How to hang up depends on when and who
After call is set up
  either party sends BYE request
From caller, before call is accepted
  send CANCEL
  BYE is bad since it may not reach the same set of users that got INVITE
  If call is accepted after CANCEL, then send BYE
From callee, before accepted
  Reject with 486 Busy Here
C
S
INVITE
100
Hangup
Accept
CANCEL
200 OK
200 OK
ACK
BYE
200 OK

## Slide 44: Calls, Call Legs and Transactions
Call is a set of point to point SIP relationships
  Call-ID
Call Leg (aka Dialog) is a point to point SIP relationship
  Call-ID + To + from
Transaction is a request/response
  Call-ID + To + From + CSeq
Call-ID
local participant
Remote participant
Remote participant
CSeq
CSeq
CSeq
CSeq

## Slide 45: Call Flow for basic call: UA to proxy to UA
Call setup
  100 trying hop by hop
  180 ringing
  200 OK acceptance
Call parameter modification
  re-INVITE
  Same as initial INVITE, updated session description
Termination
  BYE method
INVITE
100 Trying
INVITE
100 Trying
180 Ringing
180 Ringing
200 OK
200 OK
ACK
BYE
200 OK
RTP

## Slide 46: Addressing Scalability
Internet model for scalability
  Fast and simple in core
  Smarter towards periphery
  Example: RSVP vs. Diffserv
SIP uses Internet Model
  Stateless proxies in the core are fast
  Stateful proxies at periphery
  Call-stateful proxies at edge
SL Proxy
SF Proxy
SF Proxy
SF Proxy
SF Proxy
CSF Proxy
CSF Proxy
CSF Proxy
CSF Proxy
CSF Proxy
CSF Proxy
CSF Proxy
CSF Proxy
Core
Periphery
Edge
CSF Call Stateful SF Stateful SL Stateless

## Slide 47: Fault Tolerance
Server crashes have little effect
  No calls terminated, even for Call Stateful proxies running TCP
  Transactions in progress complete if a backup is available (SRV)
Protocol State stored in messages
  Responses always routed back
  TCP connections may even be re-opened to send responses!
  Branch parameter as a tool of the proxy
DCS State Header
  Under development
  Much like http cookies
  Will allow proxies to ask for data back in subsequent requests
  Allows fully call stateful servers that are highly recoverable!!

## Slide 48: Extensibility Model
Goal: Ensure baseline operation always works
Protocol can be extended by
  Defining new headers and semantics
  Defining new parameters and semantics
  Defining new methods
  Defining new bodies
New parameters and headers can be optional
  Safely ignored by recipient
  Spec mandates that unknown headers and params are ignored
  Maximizes interoperability
Features that must be understood are given names
Feature naming
  IANA registered
  com.microsoft.featurefoo naming
Clients can insist server understand a feature
Server can place a feature in a response if client understands it

## Slide 49: Extensibility: Client requests Feature
Feature represented by new header, parameter and/or new behavior
Client places needed feature in special header in request
  Require: want UAS to understand feature
  Proxy-require: want proxies to understand feature
If UAS or proxy doesn’t know feature, it responds with error and lists unknown features in Unsupported header
Client can resubmit request
C
S
INVITE Foo: blah-blah
Bar: la-la
Require: foo, bar
420 Bad Extension Unsupported: foo
INVITE
Bar: la-la
Require: bar

## Slide 50: Extensibility: Server wants feature
Client indicates features it understands in Supported header in request
  All features must be listed
  Always place header in every request
Server can use feature if its listed
If server applies feature in response, it includes a Require header indicating the feature
S
INVITE Supported: foo, bar
201 OK Foo: blah-blah Require: foo
C

## Slide 51: Extensibility: New Methods
Methods define fundamental behavior
Client can send request with new method
UAS rejects requests with unknown methods
  405 response
  list allowed methods in Allow header
Proxies don’t care about methods
  Proxy rules are independent of method
S
GOAWAY To: joe
405 Method Not Allowed Allow: INVITE, BYE,
OPTIONS, ACK,
CANCEL
C

## Slide 52: Extensibility: New Bodies
Bodies convey non-SIP related information about request
Body types enumerated by IANA registry
Not all bodies known to a server
When server receives request with unknown body
  415 Unsupported Media response
  Accept header lists valid MIME body types
Only used by UA!
S
INVITE Content-Type: text/foo
Content-Length: 2
aa
415 Unsupported Media
Accept: text/plain
C

## Slide 53: Security
Leverage existing mechanisms
HTTP
  Basic authentication
  Digest authentication
PGP
S/MIME
Transport Mechanisms

## Slide 54: HTTP Basic and Digest
Challenge Response
  Client sends request
  Server responds with 401 or 407 with “challenge”
  Client ACKs
  Client sends request again (higher Cseq) with credentials
  If OK, server processes, else sends 401/407 again
Mechanism is Stateless
  Don’t need to know that a challenge was issued
  Requests just contain credentials
Credentials can be cached
  Subsequent requests to the same server can contain same credentials
  If they expire, server issues 401/407
Two relationships
  Proxy Server challenges UAC
  UAS challenges UAC
Multiple credentials
  Any number of proxies and a UAS can issue challenge
  Credentials are accumulated

## Slide 55: HTTP Basic Authentication
Cleartext Password
  Base64 encoded
Not useful alone
  May be useful within a TLS connection from client to server
  Emulates http usage of client authentication
Not widely implemented
Depecated from bis
INVITE
401 Authorize Yourself
WWW-Authenticate:
Basic realm=“mufasa”
INVITE
Authorization: Basic
QWxhZGRpbjpvcGVuI==
200 OK

## Slide 56: HTTP Digest Authentication
Server challenge
  Realm (keyword for password)
  Nonce (random number, rotates periodically)
UAC Response
  Hash of username, password, realm and nonce, and also method
  Can also include body in hash
  Specifically, its H(H(username:realm:password):nonce:H(method:URI))
Why double hashing?
  Server can store H(user:realm:pass); doesn’t change
  Computes H(method:URI) combines with first
  No password or username on disk!
Response Authorization
  Responses can also contain credetials that authenticate caller

## Slide 57: PGP
RFC2543 specified security based on PGP
Provided
  Client to server authentication
  Client to server encryption
  Server to client authentication
  Server to client encryption
Uses public keys
Requires PGP community
  General problem with PGP
Requires request to be “canonicalized”
  Standardized format over which signature is computed
  Requires devices to maintain order of headers and parameters
Deprecated!
  No implementations
  Canonicalization a pain
  Other approaches more mature

## Slide 58: Coming soon: S/MIME
S/MIME is an IETF standard for email security
Provides authentication and encryption
Based on X.409 Public Key Certificates
  The kind you get from Verisign
  Some infrastructure in place
  Can be shipped with message
Big overhead
  Message contains payload, signed piece, and signature, maybe certificate
  Requires multipart
SDP
INVITE sip:u@h SIP/2.0
From: sip:bob@foo
To: sip:a@c
Content-Type: multipart
INVITE sip:u@h SIP/2.0
From: sip:bob@foo
To: sip:a@c
Content-Type: SDP
SDP text
signature
certificate

## Slide 59: Transport Security
Previous mechanisms allow for E2E Security
  Works through any number of proxies
  Proxies don’t need to be trusted
  Security within SIP layer
Hop by Hop Security Possible as well
  Proxies have trust relationship with each other
  E2E security by transitivity
    Relies on all hops doing security
Proxy
Proxy
Proxy
UA1
UA2
Secure
Tunnel

## Slide 60: Transport Security
IPSec
  UDP also
  Not widely implemented
  IKE barely supported
  Resides in OS
Requires no SIP extensions
Several techniques
  TLS/SSL
  IPSec
TLS/SSL
  Firewall and NAT Traversal
  Widely implemented
  Key exchange works
  Resides in application layer
  TCP only

## Slide 61: What about QoS?
QoS is handled orthogonally by other protocols
Signaling path isn’t same as media path at all!!
  Even set of ISPs is different
Separation allows yahoo to be a phone company
Many other apps need QOS, keep one mechanism
Voice will be negligible compared to data anyway

## Slide 62: Models of QoS for SIP
Diffserv
  users mark TOS byte in their RTP packets
  olympic service model
  total separation
  no
    admission control
    end to end signaling
    per call minute metering
RSVP/diffserv core w/ ringing holdback
  don’t ring unless resources reserved
  use RSVP in periphery
  resource reservations starts after INVITE
  ringing and continued signaling after RSVP done

## Slide 63: Quality of Service
SIP is “not” a Reservation Protocol, but. . .
Need Coupling Between Signaling and Reservation
  Do not ring phone until resources reserved
Uses a new extension to SIP
  INVITE contains a header that indicates there is a precondition to ringing the phone
  Preconditions include
    QoS establishment
    Security
  When preconditions met, COMET request is sent
  Phone can then ring
INV
183 Progress
PRACK
Caller
Callee
200 OK
ACK
Resource Reservation
Media
Ringing
Pickup
COMET
200 OK

## Slide 64: Information Resource
Jonathan Rosenberg
  jdrosen@dynamicsoft.com
  +1 973-952-5000