## Slide 1: Voice over IP – A Beginners Guide
Dr. Jonathan Rosenberg Vice President and Chief Technology Officer of Collaboration at Cisco Systems

## Slide 2: About Me
Bachelors and Masters 1994
Electrical Engineering
PhD, Voice over IP 2001

## Slide 3: Member of Technical Staff, Bell Laboratories, Holmdel

## Slide 4: Birthplace of the Transistor
Coincidence or on Purpose?
You decide!
Water Tower at Holmdel Site
Transistor

## Slide 5: Chief Technology Officer, dynamicsoft
Acquired 2004
Left 2009

## Slide 6: Chief Technologist, Skype
Left 2012

## Slide 7: CTO, Collaboration at Cisco

## Slide 8: Co-Inventor and Lead Author of the Session Initiation Protocol (SIP)
SIP is the fabric that connects all modern telecom products and services
Billions and billions of minutes of calls
The Phone Network is ~50% converted to SIP and will be completely built on SIP by 2020ish

## Slide 9: My Career Mission
To Reimagine Telecommunications in the
Image of the Internet

## Slide 10: Awards and Accomplishments
~125 filed,
89 Granted US Patents
71 Internet Standards,
8th most prolific creator of Internet standards of all time
Named to TR35 in 2002, along with Sergey Brin, Larry Page, John Carmack
2015 Ohio University Strowger award for pioneering contributions to telecommunications

## Slide 11
jdrosen on Steam
135 titles!
Half Life 2
World of Warcraft
Portal 2
Ori and the Blind Forest
Alice: Madness Returns
The Last of Us
Uncharted 3
Rise of the Tomb Raider
Tomb Raider (2013)
Portal 2
Prince of Persia: Sands of Time
Doom (2016)
Prince of Persia: The Forgotten Sands
Limbo
Portal
Legend of Zelda: Link Between Worlds
Guitar Hero III
God of War III
Bioshock
The Talos Principle

## Slide 12: Where I work Now: Cisco
Not This Sysco

## Slide 13: Where I work Now: Cisco
This Cisco

## Slide 14: Cisco Fast Facts
CEO: Chuck Robbins
Headquarters: San Jose, CA
Yearly Revenue: $49.1 Billion 2016
Market Capitalization: $158B
Employees: ~75,000

## Slide 15: So… what does it make?
Cisco Makes all of the Stuff Under the Hood that Makes the Internet Work
WiFi Access Points for
Businesses
All the Stuff that AT&T use to
Provide you Internet access
The Stuff that Walmart uses to connect its stores and customers
A Data Center

## Slide 16: What My Business Unit Does: Collaboration
Phones and Phone Control Software
(Freehold Township School District is a customer!)
Web Conference
Calling
Telepresence Systems
$4B Yearly Revenue
Spark Board

## Slide 17: A Quick Pitch…
Cisco Spark – FREE!
1-1 and persistent group chat up to 5000 people
Voice and video calling
Schedule meetings, ad-hoc meetings
File sharing and in-app preview
Photo sharing

## Slide 18: What is Voice over IP?
Making Voice and Video Calls using
Your Internet Connection
Instead of your Phone Line
IP == The Internet Protocol – the
Core Technology of the Internet

## Slide 19: The Internet vs. the Phone Network
Phone Network: Circuit Switched
Like a wire between users
Internet: Packet Switched
Routes messages between users

## Slide 20: Why Use Internet for Calling Instead of Phone Network??
Cheaper calls
As a business, one network instead of two
Better experiences (video!)
Mobility – receive my calls anywhere I have Internet

## Slide 21: How does it work?
Your Internet Provider’s Network
To Other Networks
Access: DSL, Cable,
Fiber

## Slide 22: Packet Switching
Your computer
Facebook.com
Web Server

## Slide 23: Packet Switching
To: fb
From: Josh
Subject: web
Please fetch www.facebook.com/index.html
Internet Protocol (IP) Packet
Header
Payload

## Slide 24: Packet Switching

## Slide 25: Packet Switching
Router looks at the destination address and makes a routing decision
?
?

## Slide 26: Packet Switching
Packet moves from hop to hop until it reaches destination

## Slide 27: A Real Packet
To: fb
From: Josh
Subject: web
Please fetch www.facebook.com/index.html
The packet is sent bit at a time. We write it this way – showing each consecutive 32 bits as a row
IP Body
Header
Body or
Payload

## Slide 28: A Real Packet
To: fb
From: Josh
Subject: web
Please fetch www.facebook.com/index.html
This set of 32 bits is the destination address – it’s the “To” part of the packet.
IP Body
Header
Body or
Payload

## Slide 29: A Real Packet
To: fb
From: Josh
Subject: web
Please fetch www.facebook.com/index.html
This set of 32 bits is the source address – it’s the “From” part of the packet.
IP Body
Header
Body or
Payload

## Slide 30: A Real Packet
To: fb
From: Josh
Subject: web
Please fetch www.facebook.com/index.html
This set of 16 bits is the protocol – it describes what comes next in the packet. It’s the “Subject” part of the packet – part of it at least.
IP Body
Header
Body or
Payload

## Slide 31: Sidebar - what is a Protocol?
A communications protocol is a system of digital rules for data exchange between computers through a computer network
Syntax
rules to encode and decode data
Type of language called ABNF which specifies protocol syntax, here for the SIP protocol
Semantics
rules to process data
A formal model of protocol semantics using a Finite State Machine (FSM) – here for SIP transactions.

## Slide 32: Why do we need Protocols?
Protocols describe the behavior of software which allows computers to talk to each other successfully to accomplish a task
Protocols need to be rigorous since computers are literal – protocols specify rules that are meant for a computer to process
Protocols need to deal with problems that might happen when computers talk to each other – loss, delay, jitter, different versions of software
Protocols are defined by a combination of computer programs (often in special languages) combined with English prose
Protocols are often standardized – agreed upon by a formalized community of computer scientists – enabling different companies to make products that work together

## Slide 33: You Use Protocols Everyday
Protocol Name | Used For | Standardized In
IP – the Internet Protocol | Exchanging packets between routers | http://www.ietf.org/rfc/rfc791.txt
HTTP – the Hypertext Transfer Protocol | Requesting and transferring documents from a web server to browser | http://www.ietf.org/rfc/rfc2616.txt
DNS – the Domain Name System | Allowing a computer to convert a human readable name (like www.twitter.com) to an IP address | https://www.ietf.org/rfc/rfc1034.txt
SMTP – the Simple Mail Transfer Protocol | Sending mail between two computers | http://www.ietf.org/rfc/rfc2821.txt
TCP – the Tranport Control Protocol | Reliable transmission of a stream of bytes | 

## Slide 34: Where do the protocols on the Internet come from?
The Internet Engineering Task Force (IETF)
An informal collection of engineers and computer scientists from around the world that define the rules that govern the Internet and oversee its operation
In existence since 1986
The standards it produces are called RFCs
8174 RFCs produced so far

## Slide 35: An Example Page of SIP
And now back to the IP packet…..

## Slide 36: The IP Address
Every device on the Internet has an IP address
The IP address is 32 bits long and uniquely identifies the device on the Internet
If a device has multiple connections to the Internet (think: your iPhone has WiFi and LTE), it has one IP address per connection – this is called an interface
The routers and switches themselves also have an IP address – one on each interface
With 32 bits there are 232 IP addresses available – or 4.2 Billion addresses – and we’re almost out of them!!

## Slide 37: IP Address Notation
31.13.69.228
This is the actual IP address of facebook.com in the US
We write it as four numbers separated by periods
Each number is between 0 and 255.
That’s 256 numbers, or 28
Four numbers, each of
Which has 256 values, gives us all 232 addresses

## Slide 38: IP Address in Iron Man 3!
Hmm – what’s wrong with this?

## Slide 39: IP Address Blocks
Notation | Means | Number of addresses in this block | Known as
173/8 | The 224 addresses from 173.0.0.0 to 173.255.255.255 | 224 = 16.7 million | Class A network
173.252/16 | The 216 addresses from 173.252.0.0 to 173.252.255.255 | 65,636 | Class B network
173.252.110/24 | The 28 addresses from 173.252.110.0 to 173.252.110.255 | 256 | Class C network

## Slide 40: IP Address Assignment
IANA is the international body that oversees all IP address allocation. They allocate large blocks to:
Regional Internet Registries (RIRs)
The RIRs, which manage geo-specific allocation to:
ISPs, which then allocates one to
Your internet router

## Slide 41: IP Address Map
Each little block represents a /8 –They are now all allocated.

## Slide 42: Back to Routers for a Moment
Packets arrive at the inputs and are moved to the correct output

## Slide 43: Back to Routers for a Moment
But what if more than one of the inputs needs to go to the same output?

## Slide 44: Queues
The router has buffers, also called queues – which holds packets until they can be sent

## Slide 45: Uh Oh - Congestion
If a the queue is full when the next packet shows up – its dropped! This is called congestion, and it causes packet loss.

## Slide 46: Uh Oh - Delay
Congestion also causes delay. If there is a lot of packets in the queue, the new packet has to wait a bit to get sent. If there arent any packets, it can get sent fast.

## Slide 47: More Delay – that Pesky Speed of Light!
Speed of light in vacuum = 300,000 km/s (186,000 miles/sec)
Speed of light in an optical fiber = 200,000 km/s
Distance from Sydney to New York = 16,000 km
Time for speed of light to travel from Sydney – New York = 80ms
80ms is a lot – more soon!

## Slide 48: More Uh Ohs - Jitter
Jitter is defined as variation in delay
Packet Number | Delay
1 | 33ms
2 | 31ms
3 | 40ms
4 | 39ms
Jitter is 9 ms
(40ms – 31ms)

## Slide 49: Back to The IP Packet
This set of 16 bits is the protocol – it describes what comes next in the packet. It’s the “Subject” part of the packet – part of it at least.
IP Body

## Slide 50: The Two Big Protocols – TCP and UDP – the Middleware of the Internet
The Transmission Control Protocol (TCP)
The Unreliable Datagram Protocol (UDP)
Stream Oriented – sequence of bytes
Packet Oriented – sequence of packets
Reliable – Retransmit lost data
Unreliable – no retransmissions
Rate control – limits how fast you can send to not clog the Internet
No Rate control – care needed not to clog the Internet
Connection oriented – computers exchange messages to “set it up” first and “end it” when done
Connectionless – just send it and go

## Slide 51: Protocol Layering
Internet Protocol
UDP
TCP
HTTP
SMTP
DNS
RTP
Each protocol runs “on top of” the ones below

## Slide 52: Analogy for Protocol Layering

## Slide 53: Protocol Layering
IP Body
IP Header
TCP Body
TCP Header
HTTP Body
HTTP Header

## Slide 54: On-the-Wire
First we send these bits – the IP header
The body of the IP packet is a TCP message – so next we send the TCP header
The body of the TCP message is the content to send – an HTTP message. It is the HTTP header, followed by the HTTP body

## Slide 55: And Now – Voice over IP
Josh’s
Surface
Jordan’s
iPhone
Skype
Server

## Slide 56: What we want to Happen
Did you see my new computer?
Did
You
see
my
new
Packets containing Josh’s words
Fast!

## Slide 57: How Fast?
Good
OK
Bad

## Slide 58: Software Components
Analog to Digital
Echo Cancellation
Noise Removal
Gain Control
Speech Encoder
Packetizer
Software on Josh’s Computer
Software on Jordan’s Computer
Depacketizer
Speech Decoder
Loss Recovery
Jitter Buffer
Digital to Analog
Network introduces delay, loss, jitter

## Slide 59: Software Components
Analog to Digital
Echo Cancellation
Noise Removal
Gain Control
Speech Encoder
Packetizer
Software on Josh’s Computer
Software on Jordan’s Computer
Depacketizer
Speech Decoder
Loss Recovery
Jitter Buffer
Digital to Analog
Network introduces delay, loss, jitter

## Slide 60: What is “Analog”?
An analog signal is a variable voltage on a wire, often measuring something in the real world
Examples:
  The wiring in your home
  The output of an electro cardiogram that measures your heartbeat

## Slide 61: Speech Starts out as Analog Too

## Slide 62: Analog to Digital - Sampling
Every XX milliseconds, record the value of the analog signal using a binary number of length YY bits
XX milliseconds

## Slide 63: How often do we need to sample?
A famous math theorem shows that – we need to sample twice as often as the highest frequency of the signal
Signal repeats every second
We need to sample twice a second

## Slide 64: So – what is the highest frequency in voice?
Frequency
20Hz
20,000Hz
4000Hz
Most speech is below 4000Hz
But not all
Range of Human Hearing
Range of Human Speech
Teenage hearing

## Slide 65: The Big Decision 60 Years Ago
Conversion of telephone network from analog to digital in 1950s
AT&T Engineers decide to cut off all speech above 4kHz
Send digital speech through phone network with 8 bits per sample
(8 bits * 2 * 4 kHz) = 64 kbps

## Slide 66: And so all speech on the phone network is like this
Frequency
20Hz
20,000Hz
4000Hz
Everything above 4kHz is gone
Range of Human Speech
This is called Narrowband Voice.

## Slide 67: With Voice over IP we can do better.
Frequency
20Hz
20,000Hz
4000Hz
Skype, Facetime and others keep it all.
Range of Human Speech
This is called Wideband Voice.

## Slide 68: Does it Matter? You decide!
Narrowband Voice
Wideband Voice

## Slide 69: Software Components
Analog to Digital
Echo Cancellation
Noise Removal
Gain Control
Speech Encoder
Packetizer
Software on Josh’s Computer
Software on Jordan’s Computer
Depacketizer
Speech Decoder
Loss Recovery
Jitter Buffer
Digital to Analog
Network introduces delay, loss, jitter

## Slide 70: The Echo Problem
Hi Daddy look at the butterfly
Sound comes out of the speaker
And the mic picks it up
The girl will hear what she said echoed back to her!

## Slide 71: Echo Canceller Software
Software on Ethan’s Computer
Delay
Volume Control
-
Learning Module
Set Volume
Set Delay
Learning Module figures out the acoustic properties of the room by listening

## Slide 72: Software Components
Analog to Digital
Echo Cancellation
Noise Removal
Gain Control
Speech Encoder
Packetizer
Software on Josh’s Computer
Software on Jordan’s Computer
Depacketizer
Speech Decoder
Loss Recovery
Jitter Buffer
Digital to Analog
Network introduces delay, loss, jitter

## Slide 73: Speech Coding – What is it?
Wideband Speech
300 kbps
Compressed
Wideband Speech
40 kbps
This is a lot! More than many home broadband speeds.
Compressed or coded speech takes up less bandwidth.

## Slide 74: Lossless Coding
Original Content
Coder
Decoder
Compressed Content
Original Content
In Lossless Coding, you get back the exact same thing (bit by bit) after applying compression and then decompression.
The combination of a coder and decoder is called a codec.

## Slide 75: Lossy Coding
Original Content
Code
Decode
Compressed Content
Almost Original Content
In Lossy Coding, you don’t get back the exact same thing (bit by bit) after applying compression and then decompression. Lossless compression can compress even more than lossy.

## Slide 76: Guess the Type!
??
ZIP

## Slide 77: Guess the Type!
LOSSLESS
ZIP

## Slide 78: Guess the Type!
??
JPG

## Slide 79: Guess the Type!
LOSSY
JPG

## Slide 80: Guess the Type!
??
PNG

## Slide 81: Guess the Type!
LOSSLESS
PNG
This is why PNG files are larger than JPG for the same image.

## Slide 82: How do we do lossy compression of voice?
We can remove information from the speech that we know you’re brain won’t notice!
Your brain is not like a computer.
You might hear two sounds that – to you – sound alike – even though a computer would think they are different!
The behavior of the brain in recognizing speech is very well understood

## Slide 83: But how does it work?
The encoder listens to you talk and builds a mathematical model of your vocal system!
It then sends the parameters of this model to the decoder which rebuilds the speech.
Example: your pitch – or core frequency of your voice.

## Slide 84: Encoding Speech Frames
10ms
10ms
10ms
Encoder
Your speech is broken into 10ms
frames of uncompressed speech
10ms
10ms
10ms
Each of these frames is compressed by sending the parameters of the mathematical model.
Decoding one frame however relies on having gotten the previous one!

## Slide 85: Speech Coding Fun Facts
Speech coding is an arcane field of mathematics and computer science that is understood by very few people in the world
There are many speech codecs, and they usually have funny monikers like “G.729” and “OPUS”
The codec used in most cell phone networks is called AMR and it can compress your voice as low as 4.75 kbps
Speech codecs have traditionally been different from music codecs; speech codecs due a bad job at music. This is why music-on-hold on the telephone sounds so awful

## Slide 86: Voice Activity Detection and Comfort Noise
Speech Magnitude (dB)
Speech Detected
Hang-Over
Speech Detected
Hang-Over
time
Sentence 1
Sentence 2
Typically fixed
at 200 ms
Noise Floor
Signal-to-
Noise
Threshold
Front-end
Speech Clipping
Front-end
Speech Clipping

## Slide 87: Video Coding

## Slide 88: Key Terms
Term | Description
Frame | An individual picture in a sequence that makes up the video
Frame Rate | The number of frames per second in video. 30 is excellent (TV quality)
Resolution | The number of horizontal and vertical pixels. VGA=640x480.
Interlacing | A mechanism for transmitting video by splitting a frame into two fields, one field representing the odd lines, and one the even field. This is the “i” in 1080i
Progressive | As opposed to interlaced, a method for transmitting video by sending each frame as a whole.
HD | High Def resolutions – 720p is 1280x720 with 60fps. 1080i is 1920x1080 at 30fps

## Slide 89: Key Concept: Macroblocks
Rectangular block in an image which is a basic unit of compression. Typically 16x16 pixels.

## Slide 90: Key Concept: Inter-Frame Prediction
Encode
Predict information in the current frame by looking at previous frames, possibly taking into account motion.

## Slide 91: Key Concept: Discrete Cosine Transform (DCT)
A technique for representing a macroblock by its component frequencies. Discarding the higher frequencies throws away the finer details without losing the core image.
Increasing horizontal frequencies
Increasing vertical frequencies

## Slide 92: Video Coding Fun Facts
Encoding (compressing) requires much more computational horsepower than decoding (decompressing)
Video coding is a highly patented area and this has made it very difficult for everyone to agree on which one to use
The primary video code in usage today is called H.264 and most video on the Internet uses it
Speech coding is mature and many consider it “done”. Video coding is still an area of research and innovation.

## Slide 93: Signaling
In VoIP, Signaling is the process of controlling the flow of voice and video packets.
Signaling includes discovery, setting up the call, tearing it down, and related functions.
Signaling in VoIP is done using the Session Initiation Protocol (SIP).

## Slide 94: SIP Basics
Josh’s
Surface
Jordan’s
iPhone
SIP
Server

## Slide 95: Lets Simplify
Josh’s
Surface
Jordan’s
iPhone
SIP
Server

## Slide 96: Josh Wants to call jordan@gmail.com
Josh’s
Surface
Jordan’s
iPhone
SIP
Server

## Slide 97: How does Josh’s computer find Jordan’s phone??
Josh’s
Surface
Jordan’s
iPhone
SIP
Server

## Slide 98: Registration
Josh’s
Surface
Jordan’s
iPhone
SIP
Server
REGISTER
jordan@gmail.com
I’m 1.2.3.4

## Slide 99: Registration
Josh’s
Surface
Jordan’s
iPhone
SIP
Server
jordan@gmail.com
is 1.2.3.4
Hard Drive

## Slide 100: Josh makes the call
Josh’s
Surface
Jordan’s
iPhone
SIP
Server
INVITE
jordan@gmail.com
I’m 5.4.3.2

## Slide 101: SIP Server Looks up Jordan
Josh’s
Surface
Jordan’s
iPhone
SIP
Server
jordan@gmail.com
is 1.2.3.4
Hard Drive

## Slide 102: SIP Server Sends to Jordan’s phone
Josh’s
Surface
Jordan’s
iPhone
SIP
Server
INVITE
jordan@gmail.com
I’m 5.4.3.2

## Slide 103: Ring!
Josh’s
Surface
Jordan’s
iPhone
SIP
Server
Ring

## Slide 104: Jordan accepts the call
Josh’s
Surface
Jordan’s
iPhone
SIP
Server
200 OK
I’m 1.2.3.4

## Slide 105: SIP Server tells Josh
Josh’s
Surface
Jordan’s
iPhone
SIP
Server
200 OK
I’m 1.2.3.4

## Slide 106: Voice and Video Packets sent
Josh’s
Surface
Jordan’s
iPhone
SIP
Server
Voice and
Video packets

## Slide 107: Summary
Voice over IP (VoIP) is using the Internet to make phone calls
VoIP has many benefits including cheaper calls, better experiences, mobility, and network unification
Low delay is a big requirement for VoIP
Voice and video are sent using codecs, which perform lossy compression
Setup of a call is done using signaling protocols – notably SIP