## Slide 1: Message Session Relay Protocol (MSRP)
Jonathan Rosenberg
Cisco Fellow

## Slide 2: Historical Context
SIP for IM first proposed in June 2000
Specification evolved into RFC 3428 – “MESSAGE method”, published December 2002
RFC3428 known as pager mode messaging
  Each instant message unrelated to previous – like SMS
  No “start” or “stop”
  Each message routed through proxies

## Slide 3: Drawbacks of Pager Mode IM
Message size limit at 1200 bytes due to UDP fragmentation issues
  “Who will ever need more than 640k of memory?”
  “No one will want to send large SMS”
Performance issues of every IM going through each proxy – the lesson of SMS in the SS7 network
IM security end-to-end extremely hard in pager mode
Message overhead substantial
SIP features based on INVITE primitives don’t apply for pager mode IM
Doesn’t easily support multiple devices

## Slide 4: Session Mode IM
Session mode IM treats IM like an RTP stream
Session starts and ends with an INVITE and BYE
SIP/SDP used to negotiate an IM channel directly between endpoints
  There are techniques for intermediaries, just like for RTP
IETF protocol for the actual IM session is Message Session Relay Protocol (MSRP)
UA 1
UA 2
Proxy
Proxy
SIP
INVITE/BYE
MSRP
IM Session
Mode

## Slide 5: MSRP: A Looooonnnnngggg Road
July 2001: first proposal. Actual IM protocol was RFC 3428 MESSAGE method, signaled with SDP.
Pushback on using SIP. IM Transport Protocol (IMTP) proposed in November 2001 – SIP minus unnecessary features.
IMTP perceived as a hack. Back to using MESSAGE, May 2002.
October 2002: send CPIM messages as the IM transport protocol
April 2003: CPIM alone doesn’t work; a shim protocol called MSRP is introduced, built in relay support
November 2003: Adopted as a SIMPLE working item
October 2004: Relays split off as a separate specification
September 2007: MSRP published as RFC 4975, MSRP Relays as RFC 4976

## Slide 6: MSRP Cliff Notes
Text based protocol, syntactically similar to SIP
TCP only
Defines a URI – MSRP URI – which are signaled in SDP
Provides chunking – the ability to split a message into smaller pieces
Provides delivery reports
Responses can be optionally omitted
SDP negotiation primarily concerned with supported content types
Carries arbitrary MIME content

## Slide 7: An Example Invitation
Indicates MSRP
Port and IP are IGNORED
MSRP URI indicates where messages should be sent
Allowed content types
INVITE sip:bob@biloxi.example.com SIP/2.0
To: <sip:bob@biloxi.example.com>
From: <sip:alice@atlanta.example.com>;tag=786
Call-ID: 3413an89KU
Content-Type: application/sdp
c=IN IP4 atlanta.example.com
m=message 7654 TCP/MSRP *
a=accept-types:text/plain
a=path:msrp://atlanta.example.com:7654/jshA7weztas;tcp

## Slide 8: Example MSRP Message
Request line has protocol name, transaction ID and method
To-Path indicates series of hops to recipient
From-Path has path from sender
Message ID unique per message
Byte-Range for chunking (later)
Content-Type but NO length
End of message indicator
MSRP a786hjs2 SEND
To-Path: msrp://biloxi.example.
com:12763/kjhd37s2s20w2a;tcp
From-Path: msrp://atlanta.exam
ple.com:7654/jshA7weztas;tcp
Message-ID: 87652491
Byte-Range: 1-25/25
Content-Type: text/plain
Hey Bob, are you there?
-------a786hjs2$

## Slide 9: Anatomy of an MSRP URI
msrp://atlanta.example.com:7654/jshA7weztas;tcp
Method is msrp or msrps for secure – meaning TLS on each hop
Host or IP address.
DNS Resolved using A or AAAA.
Port. No default but
2855 recommended
For firewall config.
Session ID.
MSRP URI identify a specific session. Session ID
Are unique within host – not globally unique
Others allowed in the future

## Slide 10: Basic Flow
INVITE and 183 contain MSRP of each side
Offerer opens a TCP connection to answerer by resolving answerer’s MSRP URI
Offerer sends IM to bind connection to From-Path URI
  So that answerer sends IM back over same connection
First IM can be empty or have real content
Alice
Bob
INVITE
msrp://1.2.3.4/ffd2
183
msrp://5.6.7.8/9876
TCP connect
SEND
To-Path: msrp://5.6.7.8/9876
From-Path://1.2.3.4/ffd2
You there?

## Slide 11: Framing
MSRP uses boundary framing
No length up front
Each message ends with an end-of-message marker
Marker is equal to
  7 dashes (-------)
  The transaction ID from the request line
  A +, # or a $:
    +: more chunks coming
    #: aborted message
    $: last chunk in message
Allows messages to be interrupted
Allows for messages whose length is not known up front
MSRP a786hjs2 SEND
To-Path: msrp://biloxi.example.
com:12763/kjhd37s2s20w2a;tcp
From-Path: msrp://atlanta.exam
ple.com:7654/jshA7weztas;tcp
Message-ID: 87652491
Byte-Range: 1-25/25
Content-Type: text/plain
Hey Bob, are you there?
-------a786hjs2$

## Slide 12: Chunking
All chunks have same message ID
Message ID is globally unique
Byte-Range is firstByte-LastByte/TotalBytes
1-1000
1001-2020
2020-2100
Total size: 2100
Message-ID: 87652491
Byte-Range: 1-1000/2100
Message-ID: 87652491
Byte-Range: 1001-2020/2100
Message-ID: 87652491
Byte-Range: 2020-2100/2100

## Slide 13: Interruptability
LastByte can be set to * if a chunk is interruptible
  MUST be used for chunks over 2048
To interrupt, send CRLF and end of chunk marker with continuation flag (+)
Receiver needs to be prepared for LastByte to be incorrect in case a chunk was interrupted without * LastByte
Total Length can also be set to *, and recipient will figure out length by putting together all chunks.
  Knows last chunk by $ marker
Interruptability allows sender to abort – just cut off message and terminate with #

## Slide 14: Purpose of Interruptability: HOL Blocking
Starts sending a video.
M-ID: 1
Byte-Range:
1-*/298374665
User types, “this is a neat video”
Client ends message at byte 65547
Sends new text message
MID: 2
Byte-Range: 1-19/19
This is a neat video
Transmission of file continues
MID: 1
Byte-Range: 65548-*
/298374665
Avoids a separate TCP/TLS
connection for each message or session

## Slide 15: Content Type Negotiation
Accept-types indicates supported types including container types
  Anything listed here can appear as the top-level type or wrapped in a container
Accept-wrapped-types indicates types that can ONLY appear in a container
  But doesn’t specify which container if there is more than one
Max-Size indicates largest message size
  Refers to overall message size, not chunk size
415 error response when receiving unsupported types
a=accept-types: message/cpim text/plain
a=accept-wrapped-types: text/html
a=max-size: 7665

## Slide 16: Example Container
MSRP d93kswow SEND
To-Path: msrp://bobpc.example.com:8888/9di4eae923wzd;tcp
From-Path: msrp://alicepc.example.com:7654/iau39soe2843z;tcp
Message-ID: 12339sdqwer
Byte-Range: 1-137/148
Content-Type: message/cpim
To: Bob <sip:bob@example.com>
From: Alice <sip:alice@example.com>
DateTime: 2006-05-15T15:02:31-03:00
Content-Type: text/plain
ABCD -------d93kswow+
CPIM wrapper

## Slide 17: Delivery Reports
Without a doubt the most complex part of MSRP – many options
Failure-Report header field indicates whether reports should be sent on failures
  Yes (default)
  No
  Partial
Success-Report header field indicates whether reports should be sent on successes
  Yes
  No (default)

## Slide 18: Success Reports
Sent if Failure-Report = yes in SEND
Include a Byte-Range header field indicating range of bytes received
Carries same message-ID as message being reported
Byte-Ranges in REPORT and SEND don’t have to match
  i.e., recipient can batch up reports
Status header includes response code namespace (000 is only one specified) and code
To-Path and From-Path like SEND
Extremely useful for file-transfer – allows resumption when tcp connections fail
SEND 1-20
SEND 21-30
SEND 31-50
REPORT 1-50
MSRP dkei38sd REPORT
To-Path: msrp://alicepc.e
xample.com:7777/iau39soe
2843z;tcp
From-Path: msrp://bob
.example.com:8888/9di4ea
e923wzd;tcp
Message-ID: 12339sdqwer
Byte-Range: 1-50/*
Status: 000 200 OK

## Slide 19: Failure Reports
Sent if Failure-Report = yes, partial or absent
If error known immediately at receiver, send error response
If delivery results not known, send 200 OK response (only if report=yes) and then send report later if failure
Example cases:
  Gateways to other protocols
  MSRP relays
Looks like success report
MSRP dkei38sd REPORT
To-Path: msrp://alicepc.e
xample.com:7777/iau39soe
2843z;tcp
From-Path: msrp://bob
.example.com:8888/9di4ea
e923wzd;tcp
Message-ID: 12339sdqwer
Byte-Range: 1-50/*
Status: 000 408 Timeout

## Slide 20: Transaction Responses
Only generated for SEND, not REPORT
Only sent for SEND when
  Failure-Report was yes
  Failure-Report was partial and the response is an error
SEND error responses are Hop-By-Hop
  To-Path contains a single URI – that of previous hop
Response code and transaction ID in start line
MSRP d93kswow 200 OK
To-Path: msrp://alicepc.exampl
e.com:7777/iau39soe2843z;tcp
From-Path: msrp://bob.exampl
e.com:8888/9di4eae923wzd;tcp
-------d93kswow$

## Slide 21: MSRP Security
Signaling links protected by TLS
Crypto-random MSRP URI
Msrps URI results in TLS connection for messages – but certs can be ignored (clients often won’t have them)
Clients reject messages with MSRP URI not matching those of signaling links
Provides message encryption only
Authenticity is not cryptographically assured; that requires SIP Identity (RFC 4474) or stronger

## Slide 22: MSRP Relays in Brief
Client configured with one or more relays
Connects to relay and authenticates with AUTH – digest
Relay provides an MSRP URI that client places in its SDP
Client
Relay
AUTH
Use-Path: msrp://1.2.3.4/sd8
INVITE
msrp://8.7.6.5/887
msrp://1.2.3.4/sd8
8.7.6.5
1.2.3.4