## Slide 2: Signaling: SIP

## Slide 3: SIP is one of Many
ITU H.323
  Originally for video conferencing
  The first standard protocol for VoIP
  Still in wide usage, but negative growth
MGCP
  Dumb phones controlled by smart server
  “Softswitch” – PSTN emulation view
Megaco/H.248
  Standard version of MGCP

## Slide 4: Core SIP Functions
Establishment of peer to peer sessions
Management of peer to peer sessions
  Keepalives
  Graceful and Non-graceful termination
Rendezvous
  Forking
  Search
Policy Based Routing
Loose Routing
Mobility
  Limited terminal mobility
  Device Mobility

## Slide 5: Core SIP Functions
Secure User Identification
Exchange and Management of Media Session data
User registration
Capability declaration
Capability query
Reliability

## Slide 6: SIP Technology Community
SIP
RFC3261
DNS
3263
Events
3265
Rel
3262
O/A
3264
RTP
SDP
SIMPLE
SigComp
SIP Extensions
ENUM
MIDCOM
STUN
ROHC

## Slide 7: SIP Design Philosophy
Patterned after other Successful Internet Standards
  HTTP
Don’t Reinvent the PSTN
General Purpose Functionality
Do Not Dictate Architectures or Services
It needs to work on any IP Network
Leverage the Best of Existing Standards
    URLs
    MIME
    RFC822
Scalability
Push state to the edge

## Slide 8: Basic Design
Request/Response Protocol
SIP is a Peer Protocol – all entities send requests and receive requests
Modelled after HTTP
Each request invokes method
  Main purpose of request
Messages contain bodies
Agent
Agent
request
response

## Slide 9: Transactions
Fundamental unit of messaging exchange
  Request
  Zero or more provisional responses
  Usually one final response
  Maybe ACK
All signaling composed of independent transactions
Identified by Cseq
  Sequence number
  Method tag
INVITE
100
200
ACK
BYE
200
First Transaction
Second Transaction
Cseq: 1
Cseq: 2

## Slide 10: Session Independence
Body of SIP message used to establish call describes the session
Session could be
  Audio
  Video
  Game
SIP operation is independent of type of session
SIP Bodies are MIME objects
  MIME = Multipurpose Internet Mail Extensions
  Mechanisms for describing and carrying opaque content
  Used with HTTP and email

## Slide 11: Protocol Components
User Agent
  End systems
  Hard and soft phones
  PSTN Gateways
  Phone Adaptors
  Media Servers
  Anything that originates or terminates SIP calls
Proxy
  SIP server responsible for relaying and processing requests between user agents
  Main job: where to send request next?
Back-to-Back User Agent (B2BUA)
  SIP server that terminates and re-originates SIP
  SBCs, Call Agents, etc.

## Slide 12: SIP Addressing
SIP addresses are URL’s
URL contains several components
  Scheme (sip)
  Username
  Hostname
  Optional port
  Parameters
  Headers and Body
SIP allows any URI type
  tel URIs
  http URLs for redirects
  mailto URLs
  leverage vast URI infrastructure
sip:jdrosen@cisco.com:5061;
user=host?Subject=foo

## Slide 13: The SIP Trapezoid
a.com
b.com
SIP
RTP

## Slide 14: SIP Methods
INVITE
  Invites a participant to a session
  idempotent - reINVITEs for session modification
BYE
  Ends a client’s participation in a session
CANCEL
  Terminates a search
OPTIONS
  Queries a participant about their media capabilities, and finds them, but doesn’t invite
ACK
  For reliability and call acceptance
REGISTER
  Informs a SIP server about the location of a user

## Slide 15: SIP Architecture
Request
Response
Media
1
2
3
4
5
6
7
8
9
10
11
12
Corp DB
13
14
14089023077@a.com
a.com
sp.com
b.com
14089023077@sp.com
14089023077@b.com

## Slide 16: SIP Message Syntax
Many header fields from http
Payload contains a media description
  SDP - Session Description Protocol
INVITE sip:+17327654321@example.com SIP/2.0
From: J. Rosenberg <sip:+14082321122@example.com>
;tag=76ah
Subject: Conference Call
To: John Smith <sip:+17327654321@example.com>
Via: SIP/2.0/UDP 1.2.3.4;branch=z9hG4bK74bf9
Call-ID: 1997234505.56.78@1.2.3.4
Content-type: application/sdp
CSeq: 4711 INVITE
Content-Length: 187
v=0
o=user1 53655765 2353687637 IN IP4 1.2.3.4
s=Sales
c=IN IP4 1.2.3.4
t=0 0
m=audio 3456 RTP/AVP 0

## Slide 17: SIP Address Fields
Request-URI
  Contains address of next hop server
  Rewritten by proxies based on result of Location Service
To
  Address of original called party
  Contains optional display name
From
  Address of calling party
  Optional display name
INVITE sip:+17327654321@example.com SIP/2.0
From: J. Rosenberg <sip:+14082321122@example.com>
;tag=76ah
Subject: Conference Call
To: John Smith <sip:+17327654321@example.com>
Via: SIP/2.0/UDP 1.2.3.4;branch=z9hG4bK74bf9
Call-ID: 1997234505.56.78@1.2.3.4
Content-type: application/sdp
CSeq: 4711 INVITE
Content-Length: 187
v=0
o=user1 53655765 2353687637 IN IP4 1.2.3.4
s=Sales
c=IN IP4 1.2.3.4
t=0 0
m=audio 3456 RTP/AVP 0

## Slide 18: SIP Responses
Look much like requests
  Headers, bodies
Differ in top line
  Status Code
    Numeric, 100 - 699
    Meant for computer processing
    Protocol behavior based on 100s digit
    Other digits give extra info
  Reason Phrase
    Text phrase for humans
    Can be anything
Status Code Classes
  100 - 199 (1XX): Informational
  200 - 299 (2XX): Success
  300 - 399 (3XX): Redirection
  400 - 499 (4XX): Client Error
  500 - 599 (5XX): Server Error
  600 - 699 (6XX): Global Failure
Two groups
  100 - 199: Provisional
    Not reliable
  200 - 699: Final, Definitive
Example
  200 OK
  180 Ringing

## Slide 19: Example SIP Response
Note how only difference is top line
Rules for generating responses
  Call-ID, To, From, Cseq are mirrored in response
  Branch parameter used as transaction ID
  Tag added to To field to identify dialog
SIP/2.0 200 OK
From: J. Rosenberg <sip:+14082321122@example.com>
;tag=76ah
To: John Smith <sip:+17327654321@example.com>
;tag=112
Via: SIP/2.0/UDP 1.2.3.4;branch=z9hG4bK74bf9
Call-ID: 1997234505.56.78@1.2.3.4
Content-type: application/sdp
CSeq: 4711 INVITE

## Slide 20: SIP Transport
SIP Messages over UDP or TCP/TLS or SCTP
Reliability mechanisms defined for UDP
UDP More Widely Used
  Faster
  No connection state
TCP preferred these days
  NAT
  Larger SIP messages
Reliability mechanisms depend on SIP request method
  INVITE
  anything except INVITE
Reason: optimized for phone calls

## Slide 21: Registrations
REGISTER creates mapping in server from one URI to another
REGISTER properties
  UA location in Contact
  Registrar identified in Request URI
  Identifies registered user in To and From field
  Expires header indicates desired lifetime
    Can be different for each Contact
Registrations are soft-state
REGISTER sip:example.com SIP/2.0
To: sip:89023077@example.com;user=phone
From: sip:89023077@example.com;user=phone
Call-ID: 1997234505.56.78@1.2.3.4
CSeq: 123 REGISTER
Contact: sip:89023077@1.2.3.4
Expires: 3600
sip:89023077@example.com
to
sip:89023077@1.2.3.4

## Slide 22: Registration Handling
Registrar is logical function handling REGISTER
Registrar steps:
  Authenticate
  Authorize
  Add Binding
  Lower expiration
  Return all currently registered UA (can be more than one)
SIP/2.0 200 OK
To: sip:89023077@example.com;user=phone
From: sip:89023077@example.com;user=phone
Call-ID: 1997234505.56.78@1.2.3.4
CSeq: 123 REGISTER
Contact: sip:89023077@1.2.3.4;expires=3600
Contact: sip:89023077@5.6.7.8;expires=524

## Slide 23: Forking
A proxy may have more than one address for a user
  Happens when more than one SIP URL is registered for a user
  Can happen based on static routing configuration
In this case, proxy may fork
Forking is when proxy sends request to more than one proxy at once
First 200 OK that is received is forwarded upstream
All other unanswered requests cancelled
INVITE
89023077@a.com
INVITE 89023077@1.2.3.4
INVITE 89023077@5.6.7.8

## Slide 24: Routing of Subsequent Requests
Initial SIP request sent through many proxies
No need per se for subsequent requests to go through proxies
Each proxy can decide whether it wants to receive subsequent requests
  Inserts Record-Route header containing its address
For subsequent requests, users insert Route header
  Contains sequence of proxies (and final user) that should receive request
Proxy
Proxy
Proxy
UA1
UA2
INVITE
BYE

## Slide 25: Setting up the Session
INVITE contains the Session Description Protocol (SDP) in the body
SDP conveys the desired session from the callers perspective
  Session consists of a number of media streams
  Each stream can be audio, video, text, application, etc.
Also contains information needed about the session
  codecs
  addresses and ports
SDP also conveys other information about session
  Time it will take place
  Who originated the session
  subject of the session
  URL for more information
SDP origins are multicast sessions on the mbone
  Originator of INVITE is not originator of session

## Slide 26: Anatomy of SDP
SDP contains informational headers
  version (v)
  origin(o) - unique ID
  information (I)
Time of the session
Followed by a sequence of media streams
Each media stream contains an m line defining
  port
  transport
  codecs
Media Stream also contains c line
  Address information
v=0
o=user1 53655765 2353687637 IN IP4 128.3.4.5
s=Mbone Audio
i=Discussion of Mbone Engineering Issues
e=mbone@somewhere.com
t=0 0
m=audio 3456 RTP/AVP 0 78
c=IN IP4 1.2.3.4
a=rtpmap:78 G723
m=video 4444 RTP/AVP 86
c=IN IP4 1.2.3.4
a=rtpmap:86 H263

## Slide 27: Negotiating the Session
Called party receives SDP offered by caller
Each stream can be
  accepted
  rejected
Accepting involves generating an SDP listing same stream
  port number and address of called party
  subset of codecs from SDP in request
Rejecting indicated by setting port to zero
Resulting SDP returned in 200 OK
Media can now be exchanged
v=0
o=user2 16255765 8267374637 IN IP4 4.3.2.1
t=0 0
m=audio 3456 RTP/AVP 0
c=IN IP4 4.3.2.1
m=video 0 RTP/AVP 86
c=IN IP4 4.3.2.1
Audio stream accepted, PCMU only.
Video stream rejected

## Slide 28: Changing Session Parameters
Once call is started, session can be modified
Possible changes
  Add a stream
  Remove a stream
  Change codecs
  Change address information
Call hold is basically a session change
Accomplished through a re-INVITE
Same session negotiation as INVITE, except in middle of call
Rejected re-INVITE - call still active!
INVITE
200
ACK
INVITE
200
ACK
reINVITE

## Slide 29: Hanging Up
How to hang up depends on when and who
After call is set up
  either party sends BYE request
From caller, before call is accepted
  send CANCEL
  BYE is bad since it may not reach the same set of users that got INVITE
  If call is accepted after CANCEL, then send BYE
From callee, before accepted
  Reject with 486 Busy Here
C
S
INVITE
100
Hangup
Accept
CANCEL
200 OK
200 OK
ACK
BYE
200 OK

## Slide 30: Call Flow for basic call: UA to proxy to UA
Call setup
  100 trying hop by hop
  180 ringing
  200 OK acceptance
Call parameter modification
  re-INVITE
  Same as initial INVITE, updated session description
Termination
  BYE method
INVITE
100 Trying
INVITE
100 Trying
180 Ringing
180 Ringing
200 OK
200 OK
ACK
BYE
200 OK
RTP

## Slide 31: Privacy and Identity
RFC 3325: A Private Extension for Asserted Identity in Trusted Networks
RFC 3323: A Privacy Mechanism for SIP
RFC 4474: SIP Identity

## Slide 32: RFC3325 Asserted Identity
Trust Domain
Authenticates
Caller and verifies
identity. Adds PAID.
INVITE
P-Asserted-Identity:
sip:+14089023077@a.com

## Slide 33: RFC3323 – SIP Privacy
Trust Domain
INVITE
P-Asserted-Identity:
sip:+14089023077@a.com
From: anonymous
INVITE
Privacy: id
From: anonymous
Anonymous Caller
INVITE
From: anonymous

## Slide 34: 4474: SIP Identity
Authenticates
Caller and verifies
identity. Signs Request.
INVITE
From:
sip:joe@example.com
Identity: asd87f7as66sda8z
INVITE
From:
sip:joe@example.com
Verifies
Signature
Only useful for user@domain addresses!

## Slide 35: Transfers and Dialog Movement: REFER (RFC 3515)
Joe
Alice
Bob
REFER
Refer-To: Bob
INVITE
INVITE
INVITE Bob
Referred-By: Joe
1
2
3
4

## Slide 36: Third Party Call Control (3pcc): RFC 3725
RTP
INVITE
no SDP
200
SDP A
INVITE
SDP A
200
SDP B
ACK
SDP B
1
2
3
4
5
6

## Slide 37: SIP and Quality of Service
RFC 3312: Integration of Resource Management with SIP
Problem
  How to make sure phone doesn’t ring unless resources are reserved
Solution
  SIP does not do resource reservation!
  SIP INVITE tells far side not to ring
  Both sides do regular QoS reservations
    RSVP
    PDP context activation
  UPDATE to change state
INVITE w. Preconditions
183 Progress
QoS Reservations
UPDATE w. Preconditions
180 Ringing
200 OK
ACK